Wall-type keyboard

The Receiver

The receiver is supplied together with the keyboard-type selector and is assembled on the control unit.

Here is a scheme of the receiver:

- Set the receiver in the programming phrase: SW1=ON

- Set the channel you wish to use for the code: if you choose the first channel set SW2=ON and cut the second channel off SW3=OFF; if you choose the second channel set SW3=ON and cut the first channel off SW2=OFF;

- Dial a four digit (from 0001 to 9999) with a time span of at least one second.

- Press “Canc” button to delete of “OK” button to confirm the code.

- Set the receiver in the SW1=OFF for normal functioning.

- Functioning selection of the channels (single-stable/bistable)

- If you want to use the first channel with a bistable functioning choose SW2=ON

- If you want to use the first channel with a single-stable functioning choose SW2=OFF

- If you want to use the second channel with a bistable functioning choose SW3=ON

- If you want to use the second channel with a single-stable functioning choose SW3=OFF

- The receiver can store just one code for each channel, so if you want to change it you have to repeat the procedure listed above.

Technical Features

- Relay				: 0.5A/24 Vac: 12 Vac

- Absorption			: 15 mA at rest

- Working temperatures	: from -10º to +160º

- Nr. Of channels		: 2

- Nr. Of codes			: 10.000